## Slide 1: HEO-F Mission Overview - Space System Design Concept -
November 19, 2014
ELaNa Reviews

## Slide 2: HEO-F Mission Objectives
Demonstrate the Utility and Advantages of a HEO/GTO for CubeSat Technology.
Demonstrate that a CubeSat Can Perform a Significant Communications Application Mission
  100 Simultaneous Voice Users
  36,000 km Link
  24 GHz Downlink; 10.5 GHz Uplink
  1 meter Diameter User Ground Station Dish Antenna
  < $1000 User Terminal Cost (Terminal Development is a Program Element)
Measure Propagation Effects on the Lowest Frequency H2O Absorption Line. (Vanderbilt University)
Measure the Radiation Environment of this GTO Orbit (Vanderbilt University)

## Slide 3: HEO-F Mission Objectives (2)
Demonstrate the Ability of a PPT Propulsion System to Carry Out Critical Mission Functions:
  Perigee Raising a GTO
  Mission Termination
Demonstrate the Reliability of a PPT, Low Power, Electric Propulsions System, in CubeSat Technology Environment and in a Geostationary Transfer Orbit:
  To Raise the Perigee to approximately 500 km
  To Eliminate the Spacecraft From Orbit at EOL over a Brief Period of Time (< 1 week from final burn)
To Continue to Support AMSAT and ARRL STEM Education Objectives as Already in Progress with the ARISS and FOX Spacecraft Missions.

## Slide 4: Prior AMSAT HEO Missions
AMSAT-Phase-3A
(1980 – Launch
Vehicle Failure)
AMSAT-OSCAR-10
(1983)
AMSAT-OSCAR-13
(1988)
AMSAT-OSCAR -40
(November 2000)
AO-40 Took 1 Decade
To Construct and Launch

## Slide 5: Mission Orbit(s)
Initial Orbit:
  ha = 35,786 km
  hp = 200 km
  i = 7.0° to 51°
  ω = 178°
Final Orbit:
  ha = 35,786 km
  hp = 500 km
  i = Unchanged
  ω = 180°
Removal Orbit:
ha = 35,786 km
hp = 80 km
i = Unchanged
  ω = unknown°
ΔV=31 m/sec
ΔV=
44 m/sec

## Slide 6: Spacecraft Physical Size
6U Cubesat Form Factor (But, 3 Standards Exist)
Up to 12 Kg Mass
Dimensions are provided by Innovative Solutions in Space BV

## Slide 7
36-44 watt Light Weight Solar
Array; MMA Design, LLP
(typical of 2)
Solar Array
Drive
Mechanism
24 GHz Horn
(20.0 dBi)
435 MHz
Omni
Antenna
10.5 GHz Horn
(17.2 dBi Gain)
1.270 GHz
Patch Antenna
Spacecraft
Configuration
1269 MHz
Omni
Antenna

## Slide 8: Spacecraft Internal Volume Allocation
L/UHF Transponder +TLM +CMD
X-Ka (mmW) Transponder
Vanderbilt Radiation Experiment
Avionics (3 RWs, Flight Computer,
MPPTs, BCR, PDU)
Star Tracker
μCAT PPT
(typ. of 4)
1269 MHz Monopole

## Slide 9: Spacecraft Functional Block Diagram

## Slide 10: Power Subsystem
Solar Arrays: MMA E-HaWK design; 72 watts average; 86 watts peak BOL; MPPT
Batteries: Li-Ion; 2600 mAHr Each; 11P1S;
  Capacity: 109 Watt-Hrs (3.5 V x 2.6 AHr x 12 Cells)
  Driving Requirement is Worst Case Eclipse Heating (2 hour eclipse w. 10 watt heaters) = 20 watt-Hrs
  Worst Case DoD: 18.3%
mmW Transponder Not Powered During Eclipse
L/UHF Transponder Powered During Nominal Eclipses but, not during W.C. Eclipses.
Loads Individually Switched: 3.3V, 5.0 V and 20 V (GaN SSPA)

## Slide 11
Solar Array Wings
(SAWs) – Two
MMA E-HaWK
Triple Deployment
Fits in 8.5 mm Stack
Peak Power: 86 W
Avg. Power: 72 W
TRL Level 9 by Flight
Single Axis SADA
Full 360° Control
SOLAR
ARRAY
WINGS
(SAWs)
&
SADA

## Slide 12: Power Budget

## Slide 13: Structure Design (Basic Approach)
6U System is Volume Limited; Not Mass Limited
Rigid (Thick) Exterior Wall Construction
  Machined Exterior Walls (6mm to 8 mm thick); 6061-T6
  P-POD Rails Formed by E-HaWK Solar Panel Exterior Frame
  Machined “Boss” Wall-to-Wall Interfaces; Screwed Joints
Avionics Module Span Interior Volume between Walls adding Significant Additional Stiffness.
Recent Vibration Testing on a Similar 6U demostrated a First Mode Resonant Frequency >1000 Hz

## Slide 14
P-POD Guide rails are formed
by the mechanical frame which
also holds and secures the
folded SAWs. Arrays fold
within an 8.5 mm packing
height.
Structure Design (2)
TWO FOR THE PRICE OF ONE FRAME.
3D CAD Courtesy MMA Design, LLC

## Slide 15: Mass Budget

## Slide 16: Thermal Design

## Slide 17: Attitude Control System
3-Axis Attitude Control System
Requirements:
  Accuracy & Knowledge:
    P: ± 1.0° (driven by Ka-Band antenna beam)
    R: ± 1.0° (driven by Ka-Band antenna beam)
    Y: ± 5.0° (driven by Solar Array Drive requirements
  NADIR Pointing Mode (with varying Earth size): ± 1.0°
  Safe Hold Mode: Return SADA to 0°; Spin about Y; Sun in XY Plane
  Point-on-Earth Target Tracking Mode (Optional)
  Maintain Solar Array Axis (Y) Normal to Sun at all Times
  Control SADA to Maintain Cells Normal to Sun (Full Power)
  Momentum Dumping Scheme at Perigee

## Slide 18: Attitude Control System (2)
Sinclair
RW
Sinclair
Star Tracker

## Slide 19: Attitude Control System (3) (Component Interfaces)

## Slide 20: Attitude Control System (4) (Operating Modes)
November 13, 2014
HEO-F Overview
21
De-Tumble
Mode
Safe-Hold
Mode
Propulsion
Mode
NADIR Pointing
Mode
Earth Target Tracking
Mode
(Optional)
Earth Center ±1°
Commanded Earth Target ±1°
At Apogee; Ram or Wake ±1°
Set SADA = 0°; Spin about Y; Sun in XZ Plane

## Slide 21: Flight Computer (IHU) (Has Flight Heritage from FOX Program)
STMicroelectronics STM32L151VBT6
ARM3 Cortex CPU (32-bit)
Up to 33 MIPS @32 MHz
Designed for ultra low power consumption
128K FLASH program memory
16K RAM (Will Likely Need More RAM)
Built-in timers, RTC, D/A, A/D, serial IO

## Slide 22: Primary Experiment - mmW Regenerative Transponder -
10.45-10.50 GHz Amateur Band Currently Actively In Use – Makes a Good Uplink Band. Many Transmitters are Available.
24.00-24.05 GHz Amateur Band not Used Very Much – Will Make a Good Downlink Band
But, 24 GHz is nearly ON the first Water Absorption Line.
This makes transmitting on this frequency much more interesting as it allows us to “see” weather with our transponder.

## Slide 23
Primary Experiment mmW Regenerative Transponder (2)
10.45-10.50 GHz
Multicarrier
RX
High Speed
ADCs
Single Carrier
BPSK 24 GHz TX
+ Turbo Code Encoder
Fast DSP
Of
FPGA
10.5 GHz Horn (17 dBi)
24 GHz Horn (20 dBi)
Uplink:
100 Users; Contention Based FDMA
Users Select Frequency Radomly
Conflicted Users Retry on Random Freq.
User TX is 2.0 watts
User Antenna is 1 meter dish
FEC on Uplink: R=1/2 Sequetial + RS
Spectral Efficiency ≈ 0.5 bit/Hz
User Rate = 5000 bps = 10 kHz
Uplink RX FFT Used to Find Each User within ms, capable of 100 sequential acquisitions..
Downlink: 10 W GaN 24 GHz SSPA
Uplink data streams aggregated into
a single downlink bit stream.
100 Users x 5,000 bps = 0.5 Mbps D.R.
Downlink Heavily Coded: R=1/6 Turbocode
Modulation is surpressed carrier BPSK
Simbol Rate = 3Msps
Bandwidth approximately 7.5 MHz
Each User Can Decode Any 5 kbps
Bit Stream
Primary User Interface is Codec-2 Vocoder
Horn Beamwdith ≈ Earth Coverage

## Slide 24: Primary Experiment mmW Regenerative Transponder (3) Uplink Signal Processor (How Do We Know It Can Be Done?)
NVIDIA Tegra K1 GPU

## Slide 25: Primary Experiment mmW Regenerative Transponder (4) 24 GHz GaN SSPA (How Do We Know It Can Be Done?)
27.5 - 31 GHz 9W Power Amplifier
TRIQUINT
Part # TGA2595

## Slide 26: mmW Transponder Uplink (Reference)
Ref: Boulder, CO @ 10° Elev. Angle; Clouds, No Rain

## Slide 27
mmW Transponder Downlink (Reference)
Ref: Boulder, CO @ 10° Elev. Angle; Clouds, No Rain
100 Users @ 5.0 kbps each

## Slide 28
mmW Transponder Downlink (Typical Conditions)
Ref: Boulder, CO @ 40° Elev. Angle; Clouds, No Rain
100 Users @ 5.0 kbps each

## Slide 29: T & C; L-to-U Transponder
UHF Telemetry Downlink (On XPDR Subcarrier)
9600 BPSK (Carrier Surpressed)
Required TLM G.S. Gain: 17.1 dBi (e.g. Standard Yagi Antenna)
L-band Command Uplink (On Uplink Sub-band)
Required Uplink Power for CMD: 25 watts
Required CMD G.S. Antenna Gain: 17.1 dBi (e.g. one M2 Yagi)
Link Margin at Apogee: >6 dB both directions
R=1/2 Sequncial (e.g. Viterbi ) + Block Code (e.g., RS) Used [Both Links]

## Slide 30
L-Band to UHF Transponder
  Active Below 5000 Km Altitude (Thru Perigee Typical)
  Monopole on TX (shared with TLM subcarrier)
  Uplink (Patch for NADIR Use and Monople Otherwise)
  T&C Active at All Times
  UHF SSPA: ≥ 1.0 watts
  L-Band LNA: ≤ 1.0 dB NF (75 K) 225K system N.T.
  User Passband: 40 to 50 KHz
T & C; L-to-U Transponder
Beacon
TLM Subcarrier at -10dB while XPDR is on
Transponder Passband

## Slide 31
TLM Link Budget
(@Apogee; Elevgle = 10°)
Circularly Polarized Yagi
C

## Slide 32
CMD Link Budget
(@Apogee; Elevgle = 10°)
C

## Slide 33: RadFx Experiment Vanderbilt University
Vanderbilt researchers are investigating the SEU sensitivity of carefully selected digital devices.
Models developed will allow estimates of the cross sectional area of a single device cell for protons capable of generating SEUs.
SEUs will be evaluated as a function of supply (bias) voltage and orbit radiation inputs.
The RadFx unit is a copy of that being flown in 2015 on the Fox-1 Cubesat.
The radiation environment, however for GTO is quite different. (See Feasibility Rev.)
Figure 5. Simulated and experimental proton cross sections
of a 65 nm SRAM cell. Model provides good agreement at high
energy and captures the steep increase in cross section at low energy.

## Slide 34: Precipitation Attenuation Experiment Vanderbilt, Department of Atmospherics
Experiment will Measure the Attenuation of a Special Beacon provided by the mmW Transponder on its Downlink Path. Careful Calibration of Amplitude and Phase Noise measurements will be made of this beacon prior to launch.
The power level of the beacon will be adjustable by ground command (from a level of +3o dBm to 0 dBm) Amplitude level will be measured, recorded, time-tagged by the IHU for subsequent TLM downlink.

## Slide 35
IHU Beacon Control
Transponder Downlink
Modulation Limit (10 MHz)
Precision Injection
Beacon
Precipitation Attenuation Experiment
24.001 GHz
24.01 GHz
22.800 – 24.000 GHz
(TBD)

## Slide 36: Pulse Plasma Thruster (μCAT ) George Washington University, Wash. DC
Micro-Cathode Arc Thruster (µCAT) micro-propulsion subsystem is an outgrowth of GWU Micropropulsion and Nanotechnology Laboratory (MpNL) research.
The technology here will be used in two mission-critical phases
  Perigee raising or maintenance
  Mission Termintation (By lowering perigee at EOL)
Total ΔV Requirement is approximately 75 m/sec
  31 m/sec for perigee raising
  44 m/sec (or less) for mission termination
Four Thrusters will be employed in Off-Pulse mode to control attitude during the active maneuver.

## Slide 37
Typical of 4 Units
Pulse Plasma Thruster
(μCAT)

## Slide 38: Total Integrated Dose (TID) Radiation Monitor (AMSAT-NA)
Teledyne TID device will be flown to continuously monitor the in-flight cumulative dose.
Unit selected has a wide range of dose-rate settings.
Interface to S/C via A/D and I2C Telemetry Bus. Simple analog output.